## Slide 1
Speaker: 王景平 / 黃其澤
Advisor: Prof. Jiin Lai
Date: 2022/12/29
Application Acceleration
with High-Level Synthesis
高階合成技術於應用加速
Team 06
Message Communication

## Slide 2: Outline
Project Goal
Background
Implementation
  QOI
  Polar Code
  Simulated Channel (AWGN)
Results
Analysis

## Slide 3: Project Goal
Target: Full run including Encoding, Channel Simulation, and Decoding
Source Coding
  Reduce the latency and energy of transmitting
    QOI (Image)
Channel Coding (Error Correction Code)
  Reliable information transmission
    Polar Code
Noisy Channel
  BPSK Modulation
  Simulated AWGN Channel
Lossless Message Compression
Delivering Information Reliably
End-to-End On Board

## Slide 4: Background
The Quite OK Image Format (QOI) is a specification for lossless image compression of 24-bit (8 bits per color RGB)
  First announced on November 24th 2021
Create an open source, faster, lossless compression method than PNG
  20–50x faster encoding, and 3–4x faster decoding speed compared to PNG
Source Coding
Channel
Coding

## Slide 5: Background
Polar code is a kind linear block error-correcting code
  Distribute the some part of channel capacity to others by polar transform
  Transmit frozen message on low reliability channels to protect the information on high reliability channel
Proposed on 2008 by Arikan
  First code with explicit construction to provably achieve the channel capacity
Polar Transform
Channel Polarization
Source Coding
Channel
Coding

## Slide 6: QOI
Lightweight Image Compression Format
Source Coding
Channel
Coding

## Slide 7: Spec
5 cases
  RUN(same as previous one)
  INDEX(seen previously)
  DIFF(difference less than 2)
  LUMA(difference less than 32/8)
  RGB(default fallback)
Must be processed in sequential order
  Output based on previous pixel
Indefinite length of output
Source Coding
Channel
Coding

## Slide 8: Polar Code
Error correction code
Source Coding
Channel
Coding

## Slide 9: Polar Encoding
Frozen bit insertion inserts zeros to more worse channel
  Reduce the influence of noise in synthetic channel
Matrix Multiplication
  Encode the message through multiplying with generator matrix
Bit Reversal
  Reverse the bit channel order to fit encoding sequence
Polar Encoder
Frozen Bit
Insertion
Matrix
Multiplication
Bit
Reversal
Source Coding
Channel
Coding

## Slide 10: Matrix Multiplication
Multiply the message with generator matrix and exchange those with bit reversal order
  Aggregate information on high reliability channel to low reliability channel
  Low reliability channels are frozen, the message on it is ensured to be 0
Bit
Reversal
Frozen Bit
Insertion
Code Rate = 1/2
Matrix Multiplication
Source Coding
Channel
Coding
Kronecker power of polar transform

## Slide 11: Polar Decoder
Polar Decoder
PE
Array
Routing
PE
Array
…
Source Coding
Channel
Coding
Routing
Routing
Routing
Unified PE Structure and Reusing
Encode Structure
Decode Structure

## Slide 12: Belief Propagation
Parallel compute LLR between every stage by propagate belief
  Prior- Knowledge ( Reliability Sequence & Receive LLR )
* LLR: Log Likelihood Ratio
Source Coding
Channel
Coding
stages
LLR
LLR
Initialization
Transmit Message
Receive Message
1 Iteration = R + L Belief Propagation
Notes: 10 / 1

## Slide 13: Modulation & AWGN Channel
BPSK modulation
AWGN
  Box-Muller Transform
    Conversion
      Uniform Distribution  Gaussian Distribution
dst_noise[i] =
(1-2*(float) dst[i]) * SNR + noise;

## Slide 14: Problem Encountered
hls::stream causes cosim hanging
  With/without dataflow
pragma HLS STREAM failed due to memory limitation to csim
  Use array buffer with pragma HLS STREAM implies FIFO in synthesis, but a relative large array in csim, which exceed the memory limitation and cause segmentation fault
  Image size is forced to reduced to 32 x 32 x 3
Even array buffer with pragma HLS STREAM causes cosim hanging
  Some code in the design may not fit well in FIFO design
Warning: OPMODE Input Warning: The OPMDOE 0110x0x …
  Can be ignored, but occupies console output and causes slow cosim
  Skip cosim, export RTL directly

## Slide 15: Result
Due to the previous issue, no much optimization is performed
Many improvements available
  FIFO design
  Dataflow
  Array partition
  Loop unrolling

## Slide 16: DEMO
An image passes through QOI encoding, Polar encoding, AWGN channel simulation, Polar decoding, QOI decoding, and print on the screen (PYNQ)
  SNR, iteration are configurable

## Slide 17: Reference
[1] https://qoiformat.org/
[2] E. Arkan, " Channel polarization: A method for constructing capacity achieving codes for symmetric binary-input memoryless channels,'' IEEE Trans. Inf. Theory, vol. 55, no. 7, pp. 30513073, Jul. 2009.
[3] E. Arýkan, " Polar codes: A pipelined implementation,'' in Proc. 4th Int. Symp. Broadband Commun. (ISBC), Jul. 2010, pp. 1114.
[4] Yu, Yongrun, et al. "Belief propagation bit-flip decoder for polar codes." IEEE Access 7 (2019): 10937-10946.
[5] Y. Shen, W. Song, Y. Ren, H. Ji, X. You and C. Zhang, "Enhanced Belief Propagation Decoder for 5G Polar Codes With Bit-Flipping," in IEEE Transactions on Circuits and Systems II: Express Briefs, vol. 67, no. 5, pp. 901-905, May 2020

## Slide 18: Decoding Structure
Decompose the encode structure into routing and PE array
  Reuse PE array by pre-defined routing matrix.
Routing
Routing
Routing
Unified PE Structure and Reusing / Shared Memory
Encode Structure
Decode Structure
Source Coding
Channel
Coding